Ruedi Steinmann
Master Thesis at ETH Zürich
Applying the Roofline Model
Advisers:	Prof. Markus Püschel and Georg Ofenbeck
Institute:	Institute for Computer Systems
Group:	Advanced Computing Laboratory
[Speaker Notes: Welcome]

---
Clock Frequency of Intel Processors
Source: Wikipedia
[Speaker Notes: Processors can't be fast enough. One way: increase clock frequency limited]

---
Transistor Count
Source: Wikipedia
[Speaker Notes: Other approach: more work per cycle CPUs become more complex, harder to understand Perf models of high value, insightful yet easy to understand =>Roofline To be used some measurements need to be done → no tool → implemented one]

---
Overview
- The Roofline Model
- Required Quantities
- Tool Requirements
- Tool architecture
  - Component Collaboration
  - Measurement Model
- Finding Peak Performance and Bandwidth
- Measurement Results of some Algorithm Implementations
[Speaker Notes: Explain points]

---
Memory Bandwidth Bottleneck
CPU
Core
Caches
Memory
Bottleneck
[Speaker Notes: Key observation: Bandwidth bottleneck While optimizing: change transfer volume and performance => Roofline model captures both]

---
Roofline Graph
[Speaker Notes: Roofline model is visual 2D performance model X Axis: Operational Intensity, more is better Y Axis Roofline Points Ceilings Performance Given opint and perf => throughtput Bandwidth ceiling Ridge point, Implementation left/right]

---
Required Quantities
- Performance
  - Operation Count / Execution Time
- Throughput
  - Transfer Volume / Execution Time
- Operational Intensity
  - Operation Count / Transfer Volume
- Performance Counters
[Speaker Notes: Present quantities PerfCounters=> which ones are used for our tool]

---
Tool Requirements
- Measure custom code
- Possibly multi threaded
- Measure required quantities
- Create plot
- Measure ceilings
- Run on different Intel x86 CPUs

---
[Speaker Notes: Two main components: driver and core]

---
Example: Measure roofline
point of matrix-matrix
multiplication

---
Parameters
Matrix Size
Measure Execution Time
Event Description

---
Matrix Size
Execution Time
Number of Runs

---
Execute
Measurement
Store Results

---
Execution Times

---
Process results
add data to plot
Measure other
quantities

---
Create plot data
file
Create plot script

---
Process script
Read data file
Create PDF

---
→ C++
→ Java
[Speaker Notes: Driver written in Java because: Simpler programming model Support for reflection Easier debugging Core written in C++ because: Dominant language for high performance code]

---
[Speaker Notes: MeasurementCommand has a big impact on Flexibility and extensibility → look at this in detail]

---
MMM
Matrix Size
[Speaker Notes: Kernel: which Code to execute, what parameters]

---
Performance
counter
Clock cycles
[Speaker Notes: Mesurer: What to measurer In our case: performance counters, clock cycle event]

---
Basic unit
of measurement

---
Possibly one workload
per core
[Speaker Notes: Single threaded: one workload Multi threaded: one workload per core → investigate the effects between the cores]

---
[Speaker Notes: During measurement: events. → workload start → kernel start → thread forked Measurement has list of rules, predicates, actions]

---
When workload starts
→ add measurer to each existing thread
→ add rule to start measurer when kernel starts
→ add rule to stop measurer when kernel stops
[Speaker Notes: In our example of MMM: Multi threaded kernel]

---
Finding Performance Ceilings
Performance
[Flop/Cycle]
[Speaker Notes: Reached PP for ADD/MUL Mixed: 90% No difference between SSE, Scalar, x87]

---
Finding Bandwidth Ceilings
Bandwidth
[Byte/Cycle]
[Speaker Notes: Theoretical throughput: 2.8 Write slower than read Non Temporal even slower, but half the transfer volume → twice as fast Random : 0.52 bytes/cycle **→ 122 cycles latency]

---
[Speaker Notes: VVM: low op intensity MVM: higher op intensity, since vector reused FFT: depends on problem size MMM: computationally bound]

---
[Speaker Notes: No suffix: cold cache as on slide before For each: how measured Data-Code: no memory transfer → infinite OpInt]

---
Conclusions
- The tool works
  - All requirements fulfilled
  - Already ported to Yonah, Core, Sandy-Bridge
  - Easily extensible
- Many effects remain to be explained
  - Caches not working as expected
  - High variances on transfer volume and execution time during memory transfers
- Tool will hopefully be used by a wider audience